## Slide 1: Autonomous & Manual RC Car
ITI AVR COURSE

## Slide 2: TABLE OF CONTENTS
1- | Introduction
2- | Methodology
3- | Hardware Components
4- | Software
5- | Layered Software Architecture
6- | Simulation
7- | Flowchart
8- | Project Challenges
9- | Testing Approach
10- | Future Suggestion

## Slide 3: Our Team JANA YASSER MERNA MOHAMED MAI AHMED
E-JUST UNIVERSITY
PHAROS -UNIVERSITY
ALEXANDRIA -UNIVERSITY
E-JUST- UNIVERSITY
SAMA KASSEM

## Slide 4: Introduction
The RC-Car Embedded System Project is a small-scale remote controlled car utilizing the ATmega32 microcontroller. This project integrates essential principles of electronics, programming, and mechanical design to create a functional prototype capable of wireless operation via a mobile app. The car incorporates core components such as DC motors, a motor driver, a Bluetooth module (HC-05), an ultrasonic sensor for obstacle detection, and a power supply to facilitate controlled movement and communication.

## Slide 5
Hardware Design
Software Development
Individual modules (drivers) implemented for:
Motor Control
LCD over I2C
UART (Bluetooth)
Ultrasonic Distance Measurement
Mode Switching (Manual/Auto)
Methodology
Components:
DC Motors
L298N Motor Driver
Ultrasonic sensor
Servo Motor
HC-05 Bluetooth
LCD
I2C Module.
Microcontroller : ATMEGA32

## Slide 6: Hardware Components : ATmega32 (Microcontroller) Motor Driver (L298N or H-bridge)
The central controller that runs the program, reads sensors and controls actuators.
0-1
0-2
Function: Drives the wheels forward, backward, left, and right.
Connections:
Motor Driver IN1, IN2 →
Microcontroller PB0, PB1 (Left Motor)
Motor Driver IN3, IN4 → Microcontroller PB2, PB3 (Right Motor)
ENA, ENB → PWM Pins for speed control
VCC → External 12V
GND → Common ground
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 7: 03 04 DC Motors Ultrasonic Sensor (HC-SR04)
.
Provide forward/backward movement. Connected to motor driver outputs. Speed/direction are controlled by the motor driver signals from PORTB.
Hardware Components :
Function: Detects obstacles in front of the car by sending and receiving sound waves.
Connections: TRIG → Microcontroller Pin PC0 ECHO → Microcontroller Pin PC1
VCC → +5V, GND → GND

## Slide 8: Servo (Steering) PWM (OC1A) 05 Bluetooth Module (HC-05) 06
Hardware Components :
:
Sweeps left and right to scan for an available path during obstacle avoidance.
The servo PWM uses the Timer1 output on PD5 (OC1A). Servo_SetAngle() writes to OCR1A.
Function: Provides wireless manual control via smartphone app.
Connections: TX → RX of Microcontroller (PD0)
RX → TX of Microcontroller (PD1) VCC → +5V, GND → GND
This Photo by Unknown Author is licensed under CC BY

## Slide 9: 7- LCD (16x2 with I2C expander)
Function: Displays mode (Auto/Manual)
obstacle detection, and status info.
Connections: SDA → PC4, SCL → PC5 (I2C lines) VCC → +5V, GND → GND
This Photo by Unknown Author is licensed under CC BY

## Slide 10: I2C (TWI) module 01 LCD I2C driver 02 Motor driver 03 Servo driver 04
I2C_Init() sets TWI bit rate (TWBR) and prescaler.I2C_Start(), I2C_Stop(), I2C_Write() are basic TWI operations used by the LCD driver.
Simple functions to set PORTB bits for motor direction: Motors_Forward(), Motors_Backward(), Motors_Left(), Motors_Right(), Motors_Stop().The MCU toggles bits that feed the H-bridge control pins.
Software:
Uses I2C low-level functions to send 4-bit commands through I2C expander (typical PCF8574-style LCD backpack).LCD_Init() sets up function, display on, clear screen. LCD_String() and LCD_SetCursor() are used from main().
Servo_Init() configures Timer1 for PWM (ICR1 = 2499) and enables OC1A.Servo_SetAngle(angle) maps angle to OCR1A value to sweep servo for obstacle scanning.

## Slide 11: UART module 05 Ultrasonic driver 06
UART_Init(baud) configures UBRR and frame format.UART_Receive() polls RXC flag and returns received byte. In main() the code checks UCSRA & RXC directly to read incoming Bluetooth characters.
Software:
Ultrasonic_Init() sets TRIG pin as output and ECHO pin as input.Ultrasonic_ReadDistance() triggers a 10µs pulse, times the ECHO using Timer2 counts, and converts ticks to centimeters (count/58).

## Slide 12: Layered Software Architecture LIB MCAL HAL
BIT_MATH
STD_TYPES
UART
I2C
DIO
SERVO
MOTOR
LCD_I2C
ULTRASONIC
APP
MAIN

## Slide 13
Simulation:

## Slide 14
Flowchart:

## Slide 15: Project Challenges

## Slide 16: Project Challenges
IR Sensor Logic
The IR sensor sensitivity was not consistent.
It could reliably detect both the two main colors (black and white), making intermediate readings inaccurate.
This caused the line-following algorithm to sometimes misinterpret the pat
Servo Timing Conflicts
Servo motor required precise PWM using Timer1.
Conflicts with motor speed control (previously using Timer0) caused unstable steering

## Slide 17: Testing Approach Unit Testing Functional Testing Integration Testing
Tested each hardware component individually:
ultrasonic sensor, servo motor, DC motors, Bluetooth module , LCD_12C.
Verified proper operation and accurate readings before integration
Tested each mode separately:
Autonomous mode: line following and obstacle avoidance.
Manual mode: Bluetooth control direction.
Ensured that each feature worked correctly
Combined all components and modes into the complete system.
Tested seamless switching between Autonomous and Manual modes using the mobile app button.
Verified overall car performance and correct interaction between all modules

## Slide 18: Future Suggestions
Add GPS module for outdoor autonomous navigation.
Implement vision-based line following using a camera
Add IoT Connectivity for Remote Monitoring and Control
Integrate AI/ML for Object Recognition and Decision-Making

## Slide 19: Thanks!